## Slide 1: REACT
REACT:
Event-driven
Asynchronous
Concurrent
Turing-complete
Students: Will Noble,
Aleksandar Milicevic
Supervisor: Stelios Sidiroglou PI: Prof. Martin Rinard

## Slide 2: Robotics Programming
Abstraction gap
  high-level problem, low-level implementation primitives
Typically steep learning curve, especially for hobbyists
Programming in terms of low-level primitives is tedious and error-prone
Largely non-standardized

## Slide 3
Concurrent and distributed architecture
  data races
  atomicity
  deadlocks
  shared data inconsistency
Implementation complexity
  hard to analyze, test, ensure correctness
3
Distributed, Interactive, Heterogeneous

## Slide 4: Proposed Solution
Model-based, event-driven paradigm
  global model of the entire distribute system
  simple sequential semantics
  expressive programming language
Runtime environment
  manages access to shared state
  no data races by construction
Analyses
  amenable to formal analyses (e.g., testing, security, …)

## Slide 5: REACT: Records, Contexts, Events
Records
  simple data structures
  used to represent the core data model of the system
Contexts
  encapsulate different processes (nodes)
Events
  allow robots to dynamically react to their environments
  triggered by the user, timer, whenever a condition holds, …

## Slide 6: Example: BeaverSim
Implement a beaver simulator: (inspired by the ROS turtlesim example)
  model: a beaver has position (x, y) and speed (vx, vy)
  constraint: no more than 5 beavers allowed
  every 1s positions are updated according to speed
  whenever a beavers hits a wall, its speed is reversed
  one simulator node displays current positions of all beavers
  arbitrary number of remote controller nodes

## Slide 7: Implementation challenges
concurrent access to (shared) beaver data
  from multiple remote controllers
  from timer events
  from GUI threads
1
0
2
3 4

## Slide 8: Traditional approach to timer events
fragmented implementation of whenever actions
  whenever conditions can turn true at various code points
    e.g., (1) when position is auto-updated based on speed and (2) when position is explicitly set by a remote controller
fragmented implementation of constraint checks
  have to make sure that invariants hold after every update

## Slide 9: REACT: domain-specific features
conditional events
periodic events
every(interval) {
[code to execute every interval ms]
}
whenever(condition) {
[code to execute whenever the condition is true]
}
invariants
typed events
on EventType {
[code to execute when an event of the above type occurs]
}
invariant {
[condition that must hold at all times]
}

## Slide 10: BeaverSim in REACT: model
MAX_BEAVERS = 5
MAX_X, MAX_Y = (10, 10)
record Beaver [
name: str,
x: int,
y: int,
vx: int,
vy: int
]
context BeaverSim [
beavers: listof(Beaver)
] {
invariant {
beavers.size() < MAX_BEAVERS
}
# ...
}
context RemoteCtrl {
# ...
}

## Slide 11: BeaverSim in REACT: events
event Spawn [
receiver: BeaverSim,
name: str
] {
guard { name.length() == 1 }
handler {
receiver.beavers += Beaver.new(name: name,
x: 0, y: 0,
vx: 1, vy: 0)
}
}

## Slide 12: BeaverSim in REACT: events
event ChangeSpeed [
receiver: BeaverSim,
idx: int,
dx: int,
dy: int
] {
guard { 0 <= idx < receiver.beavers.size() }
handler {
receiver.beavers[idx].vx += dx
receiver.beavers[idx].vy += dy
}
}

## Slide 13: BeaverSim in REACT: contexts
context BeaverSim [
beavers: listof(Beaver)
] {
on_start { @gui = MyGui.new; @gui.start() }
on_exit { @gui.stop() }
every(1000) {
@gui.draw_beavers(beavers)
for b in beavers { b.x += b.vx; b.y += b.vy }
}
whenever(some b in beavers | b.x < 0) {
b.x = 0; b.vx = -b.vx
}
}
1
0
2
3 4

## Slide 14: BeaverSim in REACT: contexts
context RemoteCtrl {
on start { @selected = -1 }
on KEY_0 { @selected = 0 }
on KEY_4 { @selected = 4 }
on KEY_c { trigger Spawn.new(name: ‘B’) }
on KEY_UP { trigger ChangeSpeed.new(idx: @selected
dx: 0, dy: -1)}
on KEY_DOWN { trigger ChangeSpeed.new(idx: @selected
dx: 0, dy: 1) }
on KEY_LEFT { trigger ChangeSpeed.new(idx: @selected
dx: -1, dy: 0)}
on KEY_RIGHT { trigger ChangeSpeed.new(idx: @selected
dx: 1, dy: 0) }
}

## Slide 15: Demo (implemented on top of ROS)

## Slide 16: Original TurtleSim Spawn event
spawn_srv_ = nh_.advertiseService("spawn", &TurtleFrame::spawnCallback, this);
bool TurtleFrame::spawnCallback(turtlesim::Spawn::Request& req, turtlesim::Spawn::Response& res) {
std::string name = spawnTurtle(req.name, req.x, req.y, req.theta);
if (name.empty()) { ROS_ERROR("A turtled named [%s] already exists", req.name.c_str()); return false; }
res.name = name;
return true;
}
std::string TurtleFrame::spawnTurtle(const std::string& name, float x, float y, float angle) {
std::string real_name = name;
if (real_name.empty()) {
do {
std::stringstream ss;
ss << "turtle" << ++id_counter_;
real_name = ss.str();
} while (hasTurtle(real_name));
} else { if (hasTurtle(real_name)) { return ""; } }
TurtlePtr t(new Turtle(ros::NodeHandle(real_name), turtle_images_[rand() % turtle_images_.size()], QPointF(x, y), angle));
turtles_[real_name] = t;
update();
ROS_INFO("Spawning turtle [%s] at x=[%f], y=[%f], theta=[%f]", real_name.c_str(), x, y, angle);
return real_name;
}

## Slide 17: Original TurtleSim model class
class Turtle {
public:
Turtle(const ros::NodeHandle& nh, const QImage& turtle_image, const QPointF& pos, float orient);
private:
void velocityCallback(const geometry_msgs::Twist::ConstPtr& vel);
bool teleportRelativeCallback(turtlesim::TeleportRelative::Request&, turtlesim::TeleportRelative::Response&);
bool teleportAbsoluteCallback(turtlesim::TeleportAbsolute::Request&, turtlesim::TeleportAbsolute::Response&);
ros::Subscriber velocity_sub_;
ros::Publisher pose_pub_;
ros::ServiceServer teleport_relative_srv_;
ros::ServiceServer teleport_absolute_srv_; }
namespace turtlesim {
Turtle::Turtle(const ros::NodeHandle& nh, const QImage& turtle_image, const QPointF& pos, float orient)
: nh_(nh), turtle_image_(turtle_image), pos_(pos), orient_(orient), lin_vel_(0.0), ang_vel_(0.0), pen_on_(true), pen_(QColor(DEFAULT_PEN_R, DEFAULT_PEN_G, DEFAULT_PEN_B)) {
velocity_sub_ = nh_.subscribe("cmd_vel", 1, &Turtle::velocityCallback, this);
pose_pub_ = nh_.advertise<Pose>("pose", 1);
teleport_relative_srv_ = nh_.advertiseService("teleport_relative", &Turtle::teleportRelativeCallback, this);
teleport_absolute_srv_ = nh_.advertiseService("teleport_absolute", &Turtle::teleportAbsoluteCallback, this);
}

## Slide 18: Big Idea
Generic platform for programming event-driven systems
  covers a whole class of programs
spreadsheets
cms
interactive event-driven apps
similar to
End-user programming of interactive apps
  examples: social web apps, robots
  makes simple tasks easy and difficult ones possible
REACT

## Slide 19: Status
Prototype for client/server applications
  implemented in Java
Prototype for web applications
  implemented for Ruby on Rails
Next: look for concrete robot examples
  robots are event driven, often mission critical
  adapt our paradigm to programming robots
  verify functional correctness

## Slide 20: Benefits and Future Goals
Rich programming platform
  speeds up development process
  eliminates a whole class of concurrency bugs by construction
Application in the security domain
  every field access is managed by the runtime system
  security policies can be defined independently and automatically enforced at runtime
Robot programming for end-users
Thank You!

## Slide 21: The End

## Slide 22: Hello World example
context Main {
/* trigger-event */
on Main:enter {
/* action call w/ argument */
Sys.print! msg:“Hello, world!”
/* built-in action call */
Main.exit!
}
}
Outputs: Hello, world!

## Slide 23: A more complex example
context Headbanger {
banging = 0
bangSpeed = 0
action bangHead! forTime:dur:5000 withEnthusiasm:enth {
banging = Clock.time + dur
bangSpeed = enth
}
whenever (banging > Clock.time) {
#spinhead(bangSpeed)
}
}
context Main {
on Main:enter {
Headbanger.enter!
Headbanger.bangHead! withEnthusiasm:10 forTime:10000
}
every (20000) {
Headbanger.bangHead! withEnthusiasm:20
}
}

## Slide 24: Variables
Syntax:
(public) (active) name = value
where name is the variable identifier, value is a numerical expression
public modifier allows variable to be visible outside of its own context
active modifier creates an active variable: read-only once defined, and re-evaluate their assigned expression every time they are referenced. They are implemented as in-line function calls

## Slide 25: In-depth: ‘whenever’ vs. ‘every’ events
Syntax:
whenever (condition) {
[code to execute]
}
condition: boolean expression to check
for direct reactions to changes in the robot’s environment
Syntax:
every(interval) {
[code to execute]
}
interval: numerical expression for time interval
requires some method of retrieving clock ticks
Implementation:
last_call = 0
whenever (last_call + interval
< clock_time) {
last_call = clock_time
[code to execute]
}
Whenever
Every

## Slide 26: In-depth: ‘on’ events vs. actions
Syntax:
on cntxt_name:event_name {
[code to execute]
}
Called explicitly with:
trigger cntxt_name:event_name
for reactions to user-defined circumstances
only execute if context is live
Syntax:
action name! <arguments> {
code
}
Argument syntax:
ext_name:int_name(:def_val)
Use system of constraints to ensure safety
Take dynamic arguments
Calling syntax:
context_id.action_id!
<arguments to pass>
‘on’ event
Action

## Slide 27: Embedded C
In order to implement APIs for particular robots in REACT, platform-specific code will surely be needed. Embedding native C-code into REACT source can facilitate this.
Special “C context” construct for creating libraries of C-code interfaceable with REACT, use _c_context keyword
C contexts can contain active variables or actions.
_c_context Foo {
public active c_val = “<C expression>”
action c_act! withArg:arg:50 “
[code...]
”
}
Code copied verbatim from within quotes

## Slide 28: Technical contributions
Expressive power & programming efficiency
Programming language close to the problem domain
  think in terms of simple data structures
  don’t worry about concurrency and distributed architecture
  declarative programming: say what not how
Runtime environment + code generation
  no explicit synchronization, queues, message passing
  no data consistency issues
  synthesized clients for different platforms
Amenable to tools, testing, and formal analyses
  core aspect of the system are kept succinct and formal
  important for safety/security critical systems

## Slide 29: REACT
Designed to be intuitive and easy to learn
Powerful expressiveness
Widespread applications

## Slide 30: Proposed Solution
Model-based, event-driven programming paradigm
  provides a simple declarative conceptual model
  expressive power & programming efficiency
  programming language close to the problem domain
Runtime environment
  manages access to single shared global state
  keeps everyone updated
  programs free of concurrency bugs by construction
Rich tool set
  amenable to formal analyses and automated testing
  enabled by the succinct and formal event model

## Slide 31: REACT summary
Pros
  Highly abstract  easy to learn & portable
  Flexible  can interface with native C code
  Accessible  robotics programming requires extensive technical knowledge; REACT abstractions eliminate the need for hobbyists to acquire such knowledge.
  Expressive  programs written faster, robots developed more easily
Cons
  Centralized (not designed for distributed systems)
  Sequential implementation (no concurrent events)
  No explicit data model
    data conflated with contexts